## Slide 1
HUBBLE CONNECTED
AI-Powered Dog Emotion Detection & Scenario Trigger System
Real-time Audio Intelligence for Pet Cameras on Edge Devices
Aditya Sharma | AI/ML Intern
Manager: Rahul | June 2026 – Present

## Slide 2
The Problem We're Solving
Millions of pet owners leave dogs at home. Existing cameras just show video — they don't understand what's happening. Owners can't watch 8 hours. They need the camera to be SMART.
The Gap
• Cameras show — they don't understand
• No alerts when dog is in distress
• No context: WHY is the dog barking?
• Video requires GPU — too expensive
Our Solution
• Listen to audio (not video)
• Classify dog emotion (3 classes)
• Classify environment sound (10 classes)
• Combine both → detect 5 real scenarios
• Alert owner's phone with context
Why Audio > Video
• 100× smaller (48KB vs 5MB per 3 seconds)
• Runs on CPU — no GPU needed
• Works in the dark
• Better privacy — no video of homes
• Dogs express emotions through sound
Target Hardware: Raspberry Pi 4 (4GB RAM, $35-55) — All processing on-device, zero cloud dependency

## Slide 3
How It Works — Complete Pipeline
Every 3 seconds, the system processes one audio chunk through the entire pipeline:
1
CAPTURE
Microphone records at 16kHz mono. 3-second chunk = 48,000 samples.
2
TWO MODELS RUN ON SAME AUDIO
Dog Emotion Model → "High_Arousal" (87%) Env Sound Model → "door_slam" (82%)
3
ADD TO HISTORY
Both results stored in a 60-second sliding window (last 20 chunks).
4
5 SCENARIO DETECTORS CHECK
Each detector scans the history for its specific pattern.
5
TRIGGER ALERT
If pattern matches → push notification to owner's phone with context.
KEY INSIGHT: Neither model alone can detect scenarios
"Dog is anxious" (Dog Model) = could be 10 reasons. "Doorbell rang" (Env Model) = so what? But "Dog is anxious" + "Doorbell rang" = Stranger at the door! — That's why we combine BOTH over TIME.

## Slide 4
Data Pipeline — Collection & Cleaning
Dog Emotion Data Sources
• Barkopedia (HuggingFace) — Academic dog vocalization dataset
• DogSpeak (HuggingFace) — Labeled dog sounds
• Freesound.org API — Community dog sounds (API key based)
• Custom Pygame GUI for manual labeling by ear
Environment Sound Data Sources
• ESC-50 — Environmental Sound Classification (50 classes)
• UrbanSound8K — 8,732 urban sound files (10 folds)
• Freesound.org API — Targeted queries per class
• Total: ~4,400 files across 10 environment classes
CRITICAL DISCOVERY: Massive Data Leakage in Anxiety Class
What We Found
• 600 files in Anxiety folder
• After 3-layer deduplication → only 25 unique!
• 575 were duplicates/augmented copies of same recordings
• Model was memorizing recordings, not learning patterns
• Artificial 100% accuracy on Anxiety class
How We Fixed It
• Layer 1: SHA-256 hash → exact byte duplicates
• Layer 2: Spectral fingerprint cosine similarity → near-dupes
• Layer 3: Noise floor fingerprinting → same recording session
• GroupShuffleSplit → zero source overlap in train/val
• Threshold calibrated by manually listening to files
• Result: Honest 80.5% accuracy (no inflation)

## Slide 5
Dog Emotion Classifier — WavLM + VotingEnsemble
Class Merging: 5 → 3 (Approved by Rahul)
Original 5: Aggressive, Alert, Anxiety, Bored, Playful
Confusion matrix: 98% overlap Aggressive ↔ Alert
Dogs sound identical when aggressive vs alert
Merged classes (based on arousal theory):
High_Arousal = Aggressive + Alert
Low_Arousal = Anxiety + Bored + Howling
Playful = Playful
Model Architecture
Input: 3-second audio chunk (48,000 samples)
Path A: WavLM (microsoft/wavlm-base-plus)
→ 768-dimensional embedding vector
→ Captures deep patterns (pretrained on 94K hrs audio)
Path B: Handcrafted features (librosa)
→ MFCC, pitch, RMS, spectral, onset (20+ features)
Combined → VotingEnsemble (RandomForest + HistGradientBoosting)
Accuracy
80.5%
Confidence Cutoff
60%
Below 60% →
"Neutral"
Playful F1 Fix
0.374 → 0.667
Key Decision: HuBERT → WavLM Switch
Started with Facebook's HuBERT (speech-only). Switched to Microsoft's WavLM (speech + noise + overlapping audio). WavLM's broader training makes it better for non-speech audio like dog barks. Playful F1 improved with 5-type augmentation: pitch shift ±2 semitones, time stretch ±10%, background noise injection.

## Slide 6
Environment Sound Classifier — 10 Classes, 89% Accuracy
Purpose: Detect WHAT is happening in the environment so we know WHY the dog is reacting
door_slam
doorbell
footsteps
speech
siren
car_horn
alarm
scratching
silence
background_noise
Training Details
• Datasets: ESC-50, UrbanSound8K, Freesound
• Total files: ~4,400
• Train/Val: 3,520 / 881 (80/20 split)
• Model: RandomForest on acoustic features
• Same librosa feature pipeline as dog emotion
Results
• Overall Accuracy: 89.0%
• Macro F1 Score: 0.867
• 16kHz mono WAV, 3-second clips
• Inference time: ~45ms per chunk
• No external dependencies (sklearn only)

## Slide 7
Scenario Fusion Engine — How It Works
The engine maintains a 60-second sliding window of results and checks 5 patterns every 3 seconds
Step 1: Same 3-second audio chunk → Both models run simultaneously
Dog Model outputs: "High_Arousal" (87%) Environment Model outputs: "door_slam" (82%)
Step 2: Both results added to history (deque maxlen=20 = 60 seconds)
dog_history = [("Neutral",0.9), ("Neutral",0.85), ("Low_Arousal",0.7), ("High_Arousal",0.87), ...] env_history = [("door_slam",0.82), ("silence",0.91), ("bg_noise",0.65), ("bg_noise",0.5), ...]
Step 3: Five detector functions scan the history for their specific pattern
_check_owner_left(): "door_slam" in history? + No speech? + Dog distressed? → TRIGGER _check_stranger(): Doorbell (+3pts) + Dog alert (+2pts) + Fast bark (+1.5pts) ≥ 7? → TRIGGER _check_other_dog(): Two different pitches detected? + Alternating bark? → TRIGGER _check_siren_howl(): Siren in env + Dog howling (long sustained note)? → TRIGGER _check_attention(): Low_Arousal 80%+ of 60s + No triggers + Repetitive whine? → TRIGGER
Step 4: If any detector triggers → Push notification to owner's phone with scenario name + details
Example: "🚪 Owner Left — Your dog is showing signs of separation anxiety. Distress detected for 15 seconds after door closed."

## Slide 8
Scenario Details — Owner Left & Stranger Detected
🚪 Scenario 1: Owner Left (Separation Anxiety)
Detection Method: AND-gate (ALL conditions must be true)
Condition 1: door_slam detected in last 120 seconds
Condition 2: No human speech for 60+ seconds
Condition 3: Dog High_Arousal for 5+ consecutive chunks (15s)
Condition 4: RMS energy escalating (getting louder)
Timeline example:
0:00 door_slam detected, dog = Neutral
0:03-0:27 silence, dog still Neutral (waiting...)
0:30 dog starts whining → Low_Arousal
0:33-0:42 dog gets worse → High_Arousal × 5 chunks
0:42 ★ ALL 4 conditions TRUE → TRIGGERED!
False positive handling:
• TV door sounds → check for music_television in env
• Dog playing → Playful emotion breaks distress streak
🔔 Scenario 2: Stranger Detected (Intruder Alert)
Detection Method: Scoring System (≥ 7.0 points = trigger)
Evidence scoring:
Doorbell/knock detected → +3.0 points
Dog emotion = High_Arousal → +2.0 points
Rapid barking (>3/sec) → +1.5 points
Regular rhythmic bark → +1.0 points
Unknown speech heard → +1.5 points
Dog NOT playful recently → +1.0 points
Approaching footsteps → +2.0 points
Example A (Stranger): doorbell(3) + alert(2) + fast(1.5)
+ not playful(1) = 7.5 ≥ 7.0 → ✅ TRIGGERED
Example B (Random bark): no doorbell(0) + alert(2)
+ fast(1.5) + not playful(1) = 4.5 < 7.0 → ❌ No trigger
Why scoring? Not all evidence present every time.
Enough combined evidence = confident detection.

## Slide 9
Scenario Details — Other Dog, Siren/Howl, Attention Seeking
🐕 Scenario 3: Other Dog
Pitch Bimodality Detection
Problem: 1 mic captures 2 dogs.
How to tell there are 2 dogs?
Split audio into 250ms sub-frames
Extract pitch from each frame
K-means cluster into 2 groups
If groups are >100Hz apart →
two different dogs!
Also checks: alternating energy
(call-and-response pattern)
Near-far ratio > 2.5 (our dog
is louder = closer to mic)
🚨 Scenario 4: Siren/Howl
Sequential 2-Stage Detection
Stage 1: Env model detects siren
Stage 2: Check if dog howls
Howl vs Bark (5 checks):
voiced_fraction > 0.6
(60%+ continuous sound)
duration > 1.5 seconds
(bark = 0.3s, howl = 3s+)
bandwidth < 1200 Hz
(howl = narrow, bark = wide)
pitch_range > 200 Hz
(howl sweeps up)
HNR > 8 dB
(howl = tonal, bark = noisy)
😢 Scenario 5: Attention Seeking
Absence-Based + Autocorrelation
Triggers when NO external cause
but dog is still distressed.
4 conditions (all required):
Low_Arousal ≥ 80% of last 60s
NO env triggers (no doorbell,
siren, other dog, speech)
Repetitive pattern detected via
autocorrelation (peak > 0.3)
Whine signature: pitch > 500Hz,
RMS < 0.06
Hardest scenario to detect —
defined by ABSENCE of triggers,
not presence.

## Slide 10
Testing & Results — 70% → 90% → 100%
Test Suite: 10 cases — 5 positive (should trigger) + 5 negative (should NOT trigger)
Run 1
70%
Passed: 7/10 — 3 positive tests failed
Fix: Initial run — detectors too strict
Run 2
90%
Passed: 9/10 — 1 test still failing
Fix: Fixed Stranger scoring threshold
Run 3
100%
Passed: 10/10 — All tests pass!
Fix: Fixed history reset between tests
Final Results Summary
Component
Metric
Value
Details
Dog Emotion Classifier
Accuracy
80.5%
3 classes, VotingEnsemble (RF + HistGB)
Environment Classifier
Accuracy
89.0%
10 classes, Macro F1: 0.867
Scenario Detection
Test Pass Rate
100%
10/10 — 5 positive + 5 negative
Confidence Threshold
Cutoff
60%
Below 60% → "Neutral" (Rahul's requirement)
Playful Class
F1 Improvement
+78%
0.374 → 0.667 via 5-type augmentation

## Slide 11
Edge Deployment — Raspberry Pi 4 Performance
Complete on-device processing — zero cloud, zero latency, full privacy
Latency Budget per 3-second Chunk
WavLM Inference
~800ms
Feature Extraction
~120ms
Env Classifier
~45ms
RandomForest
~5ms
Scenario Engine
<1ms
Total: ~970ms / 3000ms budget (67% headroom)
Resources & Optimization
Hardware: Raspberry Pi 4 (4GB RAM, $35-55)
RAM usage: ~260MB total (of 4GB)
Model sizes: WavLM ~90MB, Env ~5MB, RF ~1MB
Audio buffer: 192KB per chunk
Optimization options:
• DistilHuBERT: 800ms → 300ms (-3% accuracy)
• WavLM first 6 layers: 800ms → 400ms (-2%)
• Google Coral USB TPU: 800ms → ~100ms
• INT8 quantization for env model
• Voice Activity Detection (skip silence)

## Slide 12
Technology Stack
ML / Audio
• Python 3.12
• PyTorch + HuggingFace Transformers
• WavLM (microsoft/wavlm-base-plus)
• scikit-learn (VotingEnsemble)
• librosa (feature extraction)
• NumPy, SciPy
• imbalanced-learn (SMOTE)
• joblib (model serialization)
Data Pipeline
• huggingface_hub
• Freesound.org REST API
• soundfile (WAV I/O)
• Pygame (labeling GUI)
• hashlib (SHA-256 dedup)
• tqdm (progress bars)
• 3 download scripts
• Deduplication pipeline
Backend API
• Node.js + Express.js v4
• MongoDB + Mongoose v8
• JWT authentication
• RBAC (User / Admin)
• Swagger/OpenAPI docs
• Helmet, CORS, Rate limiting
• In-memory DB fallback
• 8 REST endpoints
Frontend
• Vanilla HTML/CSS/JS
• Single Page Application
• Dark glassmorphism UI
• Responsive design
• Product CRUD dashboard
• Toast notifications

## Slide 13
Future Roadmap
Short-term
• Per-dog baseline calibration
• Notification cooldown logic
• Audio clip with alerts
• Voice Activity Detection
Medium-term
• DistilHuBERT (2.5× faster)
• Learned fusion model (LSTM)
• Multi-dog support
• TFLite INT8 quantization
Long-term
• Multimodal (audio + video)
• Federated learning
• Veterinary integration
• More scenarios

## Slide 14
Thank You
Questions & Discussion
Aditya Sharma | AI/ML Intern | Hubble Connected
Dog Emotion: 80.5% | Env Sound: 89% | Scenarios: 100% test pass Edge deployment: ~970ms/chunk on Raspberry Pi 4 | All processing on-device