## Slide 1
HUBBLE CONNECTED
AI-Powered Dog Emotion Detection & Scenario Trigger System
Real-time Audio Intelligence for Pet Cameras on Edge Devices
Aditya Sharma | AI/ML Intern
Manager: Rahul | June 2026 - Present

## Slide 2
The Problem We Are Solving
Millions of pet owners leave dogs at home for 8-10 hours daily. Existing cameras just show video. They don't understand what is happening. Owners cannot watch continuously. They need smart alerts.
The Gap
Cameras show - they don't understand
No alerts when dog is in distress
No context: WHY is the dog barking?
Video requires GPU - too expensive
Our Solution
Listen to audio (not video)
Classify dog emotion (3 classes)
Classify environment sound (10 classes)
Combine both to detect 5 real scenarios
Alert owner's phone with context
Why Audio Over Video
100x smaller (48KB vs 5MB per 3 seconds)
Runs on CPU - no GPU needed
Works in the dark
Better privacy - no video of homes
Dogs express emotions through sound
Target: Raspberry Pi 4 (4GB RAM, $35-55) - All processing on-device, zero cloud dependency

## Slide 3
How It Works - Complete Pipeline
Every 3 seconds, the system processes one audio chunk through the entire pipeline:
1
CAPTURE
Microphone records at 16kHz mono. 3-second chunk = 48,000 samples.
2
TWO MODELS RUN ON SAME AUDIO
Dog Emotion Model: "High_Arousal" (87%) Env Sound Model: "door_slam" (82%)
3
ADD TO HISTORY
Both results stored in a 60-second sliding window (last 20 chunks).
4
5 SCENARIO DETECTORS CHECK
Each detector scans history for its specific pattern.
5
TRIGGER ALERT
If pattern matches, push notification to owner's phone with context.
KEY INSIGHT: Neither model alone can detect scenarios
"Dog is anxious" alone could mean 10 things. "Doorbell rang" alone means nothing. But "Dog is anxious" + "Doorbell rang 10 seconds ago" = Stranger at the door!

## Slide 4
Data Pipeline - Collection & Cleaning
Dog Emotion Data Sources
Barkopedia (HuggingFace) - Academic dog vocalization dataset
DogSpeak (HuggingFace) - Labeled dog sounds
Freesound.org API - Community dog sounds (API key based)
Custom Pygame GUI for manual labeling by ear
Environment Sound Data Sources
ESC-50 - Environmental Sound Classification (50 classes)
UrbanSound8K - 8,732 urban sound files (10 folds)
Freesound.org API - Targeted queries per class
Total: ~4,400 files across 10 environment classes
CRITICAL DISCOVERY: Massive Data Leakage in Anxiety Class
What We Found
600 files in Anxiety folder
After 3-layer deduplication: only 25 unique!
575 were duplicates of same source recordings
Model was memorizing, not learning patterns
Artificial 100% accuracy on Anxiety class
How We Fixed It
Layer 1: SHA-256 hash (exact byte duplicates)
Layer 2: Spectral fingerprint cosine similarity
Layer 3: Noise floor fingerprinting (same session)
GroupShuffleSplit: zero source overlap in train/val
Threshold calibrated by manually listening to files
Result: Honest 80.5% accuracy (no inflation)

## Slide 5
Dog Emotion Classifier - WavLM + VotingEnsemble
Class Merging: 5 to 3 (Approved by Rahul)
Original 5: Aggressive, Alert, Anxiety, Bored, Playful
Confusion matrix: 98% overlap Aggressive vs Alert
Merged into 3 arousal-based classes:
High_Arousal = Aggressive + Alert
Low_Arousal = Anxiety + Bored + Howling
Playful = Playful
Model Architecture
Input: 3-second audio chunk (48,000 samples)
Path A: WavLM (microsoft/wavlm-base-plus)
768-dim embedding, pretrained on 94K hrs audio
Path B: Handcrafted features (librosa)
MFCC, pitch, RMS, spectral, onset (20+ features)
Combined: VotingEnsemble (RandomForest + HistGradientBoosting)
Overall Accuracy
80.5%
Confidence Cutoff
60% (below = "Neutral")
Playful F1 Improvement
0.374 to 0.667 (+78%)
Model Switch
HuBERT to WavLM
Key Decisions Explained
HuBERT to WavLM: HuBERT was trained on speech only. WavLM was trained on speech + noise + overlapping audio.
WavLM is better for non-speech audio like dog barks because of broader training data.
Confidence threshold of 60%: Below this, model returns "Neutral" instead of guessing. Required by Rahul.
Playful fix: Applied 5-type augmentation (pitch shift, time stretch, noise injection) to boost underrepresented class.

## Slide 6
Environment Sound Classifier - 10 Classes, 89% Accuracy
Purpose: Detect what is happening around the dog so we know WHY the dog is reacting
door_slam
doorbell
footsteps
speech
siren
car_horn
alarm
scratching
silence
background_noise
Training Details
Datasets: ESC-50, UrbanSound8K, Freesound
Total files: ~4,400
Train/Val: 3,520 / 881 (80/20 split)
Model: RandomForest on acoustic features
Same librosa feature pipeline as dog emotion
Results
Overall Accuracy: 89.0%
Macro F1 Score: 0.867
Format: 16kHz mono WAV, 3-second clips
Inference time: ~45ms per chunk
No external dependencies (sklearn only)

## Slide 7
Scenario Fusion Engine - How It Works
Both models run on the same audio. Results go into a 60-second history. Five detectors scan for patterns.
Step 1: Same 3-second audio chunk goes to both models simultaneously
Dog Model output: "High_Arousal" (87%) Environment Model output: "door_slam" (82%)
Step 2: Both results added to history (deque maxlen=20 = last 60 seconds)
dog_history = [("Neutral",0.9), ("Neutral",0.85), ("Low_Arousal",0.7), ("High_Arousal",0.87), ...] env_history = [("door_slam",0.82), ("silence",0.91), ("bg_noise",0.65), ("bg_noise",0.5), ...]
Step 3: Five detector functions scan history for their specific pattern
_check_owner_left(): door_slam in history? + No speech? + Dog distressed for 15s? --> TRIGGER
_check_stranger(): Doorbell (+3pts) + Dog alert (+2pts) + Fast bark (+1.5pts), total >= 7? --> TRIGGER
_check_other_dog(): Two different pitches detected? + Alternating bark pattern? --> TRIGGER
_check_siren_howl(): Siren in env + Dog howling (long sustained note)? --> TRIGGER
_check_attention(): Low_Arousal 80% of 60s + No env triggers + Repetitive whine? --> TRIGGER
Step 4: If any detector triggers --> Push notification to owner's phone with scenario name and details
Example: "Owner Left - Your dog is showing signs of separation anxiety. Distress detected for 15 seconds after door closed."

## Slide 8
Scenario Details - Owner Left & Stranger Detected
Scenario 1: Owner Left (Separation Anxiety)
Detection Method: AND-gate (ALL conditions must be true)
Condition 1: door_slam detected in last 120 seconds
Condition 2: No human speech for 60+ seconds
Condition 3: Dog High_Arousal for 5+ consecutive chunks (15s)
Condition 4: RMS energy escalating (getting louder)
Timeline example:
0:00 door_slam detected, dog = Neutral
0:03-0:27 silence, dog still Neutral
0:30 dog starts whining, Low_Arousal
0:33-0:42 dog gets worse, High_Arousal x5 chunks
0:42 ALL 4 conditions TRUE --> TRIGGERED
False positive handling:
TV door sounds: check for music_television in env
Dog playing: Playful emotion breaks distress streak
Scenario 2: Stranger Detected (Intruder Alert)
Detection Method: Scoring System (>= 7.0 points = trigger)
Evidence scoring:
Doorbell/knock detected +3.0 points
Dog emotion = High_Arousal +2.0 points
Rapid barking (>3/sec) +1.5 points
Regular rhythmic bark +1.0 points
Unknown speech heard +1.5 points
Dog NOT playful recently +1.0 points
Approaching footsteps +2.0 points
Example A (Stranger): doorbell(3) + alert(2)
+ fast bark(1.5) + not playful(1) = 7.5 --> TRIGGER
Example B (Random bark): no doorbell(0) + alert(2)
+ fast bark(1.5) + not playful(1) = 4.5 --> No trigger
Why scoring? Not all evidence present every time.

## Slide 9
Scenario Details - Other Dog, Siren/Howl, Attention Seeking
Scenario 3: Other Dog
Pitch Bimodality Detection
Problem: 1 mic captures 2 dogs.
How to tell there are 2 dogs?
Split audio into 250ms sub-frames
Extract pitch from each frame
K-means cluster into 2 groups
If groups are >100Hz apart:
two different dogs confirmed
Also checks: alternating energy
(call-and-response pattern)
Near-far ratio > 2.5 (our dog
is louder = closer to mic)
Scenario 4: Siren / Howl
Sequential 2-Stage Detection
Stage 1: Env model detects siren
Stage 2: Check if dog howls back
Howl vs Bark (5 checks):
voiced_fraction > 0.6
(60%+ continuous sound)
duration > 1.5 seconds
(bark = 0.3s, howl = 3s+)
bandwidth < 1200 Hz
(howl = narrow, bark = wide)
pitch_range > 200 Hz
(howl pitch sweeps up)
HNR > 8 dB
(howl = tonal, bark = noisy)
Scenario 5: Attention Seeking
Absence-Based + Autocorrelation
Triggers when NO external cause
but dog is still distressed.
4 conditions (all required):
Low_Arousal >= 80% of last 60s
NO env triggers (no doorbell,
siren, other dog, speech)
Repetitive pattern detected via
autocorrelation (peak > 0.3)
Whine signature: pitch > 500Hz,
RMS < 0.06
Hardest scenario to detect.
Defined by ABSENCE of triggers,
not their presence.

## Slide 10
Testing & Results
Test Suite: 10 cases - 5 positive (should trigger) + 5 negative (should NOT trigger)
Run 1
70%
Passed: 7/10 - 3 positive tests failed
Fix: Initial run, detectors too strict
Run 2
90%
Passed: 9/10 - 1 test still failing
Fix: Fixed Stranger scoring threshold
Run 3
100%
Passed: 10/10 - All tests pass
Fix: Fixed history reset between tests
Final Results Summary
Component
Metric
Value
Details
Dog Emotion Classifier
Accuracy
80.5%
3 classes, VotingEnsemble (RF + HistGB)
Environment Classifier
Accuracy
89.0%
10 classes, Macro F1: 0.867
Scenario Detection
Test Pass Rate
100%
10/10: 5 positive + 5 negative
Confidence Threshold
Cutoff
60%
Below 60% returns "Neutral" (Rahul's requirement)
Playful Class
F1 Improvement
+78%
0.374 to 0.667 via 5-type augmentation

## Slide 11
Edge Deployment - Raspberry Pi 4 Performance
All processing happens on-device. Zero cloud, zero latency, full user privacy.
Latency Budget per 3-second Chunk
WavLM Inference
~800ms
Feature Extraction
~120ms
Env Classifier
~45ms
RandomForest
~5ms
Scenario Engine
<1ms
Total: ~970ms / 3000ms budget (67% headroom)
Resources & Optimization
Hardware: Raspberry Pi 4 (4GB RAM, $35-55)
RAM usage: ~260MB total (of 4GB)
Model sizes: WavLM ~90MB, Env ~5MB, RF ~1MB
Audio buffer: 192KB per chunk
Optimization options:
DistilHuBERT: 800ms to 300ms (-3% accuracy)
WavLM first 6 layers: 800ms to 400ms
Google Coral USB TPU: 800ms to ~100ms
INT8 quantization for env model
Voice Activity Detection (skip silence)

## Slide 12
Technology Stack
ML / Audio
Python 3.12
PyTorch + HuggingFace Transformers
WavLM (microsoft/wavlm-base-plus)
scikit-learn (VotingEnsemble)
librosa (feature extraction)
NumPy, SciPy
imbalanced-learn (SMOTE)
joblib (model serialization)
Data Pipeline
huggingface_hub
Freesound.org REST API
soundfile (WAV I/O)
Pygame (labeling GUI)
hashlib (SHA-256 dedup)
tqdm (progress bars)
3 download scripts
Deduplication pipeline
Backend API
Node.js + Express.js v4
MongoDB + Mongoose v8
JWT authentication
RBAC (User / Admin)
Swagger/OpenAPI docs
Helmet, CORS, Rate limiting
In-memory DB fallback
8 REST endpoints
Frontend
Vanilla HTML/CSS/JS
Single Page Application
Dark glassmorphism UI
Responsive design
Product CRUD dashboard
Toast notifications

## Slide 13
Future Roadmap
Short-term
Per-dog baseline calibration
Notification cooldown logic
Audio clip with alerts
Voice Activity Detection
Medium-term
DistilHuBERT (2.5x faster, -3% accuracy)
Learned fusion model (LSTM)
Multi-dog support via voice embeddings
TFLite INT8 quantization
Long-term
Multimodal fusion (audio + video)
Federated learning on-device
Veterinary integration
Additional scenarios (thunder, injury)

## Slide 14
Thank You
Questions & Discussion
Aditya Sharma | AI/ML Intern | Hubble Connected
Dog Emotion: 80.5% | Env Sound: 89% | Scenarios: 100% test pass Edge deployment: ~970ms/chunk on Raspberry Pi 4 | All processing on-device